## Slide 1
Distributed eblock-100C
50kW/120kWh Technical Proposal

## Slide 2
Contents
1
2
3
Product Description
Reference
BESS Proposal

## Slide 3
BESS Technical Proposal
1

## Slide 4
Customer Requirements
Item | Value | Remark
Nominal capacity | 120kWh | 
PV Power | kW | 
Load Power | kW | Normal
 | kW | Backup
Delivery Date |  | 
Operating Profile | 1 | （cycle/day）
C-rate | ≤0.5C | 
Project Location |  | 
Certification |  | 

## Slide 5
Equipment List
No | Product | Type | Unit | Qty | Remark
1 | eBlock | eBlock-100C | set | 1 | Each eBlock-100C: 50kW/120kWh PV Input（Max.）:100kW AC Output: 50kW Total capacity : 120kWh
2 | EMS | e-Mind | set | 1 | Self-Use Backup Power Supply Time of Use
This project is configured according to the DC side capacity of 50kW/120kWh

## Slide 6
Access & Installation

## Slide 7
BESS- Electrical Primary System Drawing
This project is configured according to the DC side capacity of 120kWh, and a total of 1 eBlock-100C units is required .

## Slide 8
BESS: Installation Layout Drawing

## Slide 9
BESS: Equipment base
Each device is equipped with standard equipment base, which adopts trench-free design and is easy to install and connect. Just require the cement floor surface to be flat and bearing two tons per square meter.

## Slide 10
Product Description
2

## Slide 11
eBlock-100C-CE/ EV+PV+ESS
The Best Choice for EV+PV+ESS
Power Capacity: 120kWh (AC side)
PV Input Power: Max 100kW (DC side)
Conversion Efficiency: 88%@rated working conditions (AC side)
AC output: 50kVA（400V）
Cabinet Protection: IP55
Thermal Management: Liquid cooling (PCS+PACK)
Area Coverage: 1m2
Energy Density: 120kWh/m2
Width × Height × Depth (mm) : 1000mm×2270mm×1000mm
Products Data

## Slide 12
General application scenario
PV direct access, no need for PV inverters, saving customer costs, higher system efficiency
Maximum supports up to 3 parallel cabinets with 360kWh
Maximum PV 300kW input
Self-consumption mode
Support black start
Support diesel power generation
Support the mixed use of new and old batteries.
Support DC & AC EV charging
The Block - 100C supports the direct connection of PV panels, and a single unit can form a photovoltaic, energy storage and charging system.

## Slide 13
eBlock-100C
Long life cell
Integrated high quality and high cycle life LFP cell, cycle times >10000 times
Efficient thermal management system
Integrated efficient liquid cooling system
The temperature difference is < 3℃
Actively equalizing BMS
Use efficient bidirectional equalization technology to eliminate series losses
High performance Hybrid inverter
Liquid cooling system, Multilevel topology, maximum efficiency 99.3%, integrated BMS and power distribution functions
Active safety system
Each pack is equipped with a monitoring module to realize pack-level monitoring and alarm for the battery, to ensure that the system is safe and controllable
All in One Design
LVRT / HVRT

## Slide 14
BLM System Diagram
Stratified zone design: eBlock 、eLink and eMind
BLM
eBlock
Block
Equipment
Link
Connection
Mind
Data management
PACK
BMS
ASS
eLink
Power Distribution
High Speed Communication
eMind
eMind for Cloud
eMind for Mobile
Hybrid inverter
FSS

## Slide 15
Distributed ESS eBlock features
Integrated feature：Cell +BMS+Hybrid inverter+ fire protection + liquid cooling is integrated into a standardized energy block that can be infinite AC parallel.
Control feature：eBlock self-consistent control, power coordination, flexible deployment, centralized scheduling。
JD ENERGY Distributed energy block storage solution
=/∽
Grid
=/∽
=/∽
Transformer
eBlock
1
eBlock
2
eBlock
n
120 kWhStandardized Energy eBlock

## Slide 16
Key Technology - Single Group String Integration Technique
The distributed eBlock scheme eliminates the parallel circulation and the capacity loss and greatly improves the power station income.
=/∽
PCS
2
3
4
Maximum output
eBlock
Traditional centralized energy storage
2
=/∽
PCS
2
3
=/∽
PCS
3
5
Maximum output

## Slide 17
Extreme safe
Standardized products + system safety design, so that the system safety reliable guarantee
The integrated design of Hybrid inverter and BMS eliminates protection blind spots.
In-cabinet aerosol +water firefighting system.
Cabinet fireproof material design, fireproof time is more than 2 hours.
Reliable and efficient
Passed a number of test certification
PCS is IP66 protection design, high protection brings high reliability.
PCS uses a three-level topology with a maximum efficiency of 99%。
High efficiency liquid cooling temperature control system, consumption reduced by 30%.
Series design, parallel capacity loss rate is 0
Cabinet IP55 design, the highest C5 anti-corrosion level, can cope with any harsh environment.
Core feature-Extremely safe, reliable and efficient
System efficiency ≥88%

## Slide 18
The 3-level active safety design based on the system view makes the energy storage system truly safe and controllable.
Single rack independent cabinet, cabinet fire resistance > 2 hours
Partition isolation
Safety early warning
Health assessment
Life prediction
Battery health management for AI
Inside fire protection
Key technology – Active safety design
Pack
Cell Sensor &Fuse
LFP Cell&Aerogel
cell
Rack
Temperature, VOC ,smoking detector，aerosol，
water fire fighting

## Slide 19
Reference
3

## Slide 20
Source-Grid Side Project Cases

## Slide 21
Ning XiaTong Libian Shared Energy Storage Station
200 MWh
Application Type: Utility Scale
Economic Model: Peak Shaving, Capacity Market, Axilliary Sservice
Environment Feature： High/Low Ambient Temperature，Desert
COD：2022.12
Wu Zhong City of Ningxia Province, China
eBlock 372
100 MW
Source-Grid Side
Project Capacity

## Slide 22
Ning Xia Xin Liangbian Electrochemical Energy Storage Station
200 MWh
COD：2023.06
Wu Zhong City of Ningxia Province, China
eBlock 372
100 MW
Source-Grid Side
Application Type: Utility Scale
Economic Model: Peak Shaving, Capacity Market, Axilliary Sservice
Environment Feature： High/Low Ambient Temperature，Desert
Project Capacity

## Slide 23
Guang Xi GuiGang Energy Atorage Station
288 MWh
Application Type: Utility Scale
Economic Model: Peak Shaving, Capacity Market, Axilliary Sservice
Environment Feature： High Ambient Temperature，High Ambient Humidity
COD：2023.05
Gui Gangcity, Guang Xi Province
eBlock 372
144 MW
Source-Grid Side
Project Capacity

## Slide 24
Guang Xi ChongZuo ZhongYuan Energy Storage Station
230 MWh
Project Capacity
Application Type: Utility Scale
Economic Model: Peak Shaving, Capacity Market, Axilliary Sservice
Environment Feature： High Ambient Temperature，High Ambient Humidity
COD：2023.05
Gui Gang city, Guang Xi Province
eBlock 372
115 MW
Source-Grid Side

## Slide 25
HuNan YongZhou HuangMa Energy Storage Station
2.5 MWh
Application Type: Utility Scale
Economic Model: Peak Shaving, Capacity Market, Axilliary Sservice
Environment Feature： High Ambient Temperature，High Ambient Humidity
COD：2021.11
Yong Zhou Cicty, HuNan Province
eBlock 172
1.25 MW
Project Capacity
Source-Grid Side

## Slide 26
HaiNan Yaogu Energy Storage Station
10 MWh
COD：2023.05
Hai Kou city, haiNan Province
eBlock 372
5 MW
Project Capacity
Application Type: Utility Scale
Economic Model: Peak Shaving, Capacity Market, Axilliary Sservice
Environment Feature： High Ambient Temperature，High Ambient Humidity, Near Sea
Source-Grid Side

## Slide 27
Commercial and Industrial ESS

## Slide 28
YongZhou Customer Side Energy Storage Station
1.9 MWh
Project Capacity
COD：2022.08
YongZhou City, HuNan Province
eBlock 172
0.95 MW
用户侧
Application Type: C&I
Economic Model: Peak-Valley Arbitrage, New Energy Consumption, Axilliary Sservice
Environment Feature： High Ambient Temperature，High Ambient Humidity

## Slide 29
SanWei DaTong Energy Storage Station
2.4 MWh
Project Capacity
COD：2023.05
JiaXin City, ZheJiang Province
eBlock 200
1.2 MW
用户侧
Application Type: C&I
Economic Model: Peak-Valley Arbitrage, New Energy Consumption, Axilliary Service
Environment Feature： High Ambient Temperature，High Ambient Humidity

## Slide 30
PingYao Energy Storage Station
688 kWh
Project Capacity
COD：2022.11
JingZhong City, ShanXi Province
eBlock 172
344 kW
用户侧
Application Type: C&I
Economic Model: Peak-Valley Arbitrage, New Energy Consumption, Axilliary Service
Environment Feature： High Ambient Temperature, Desert

## Slide 31
DongGuan GongShangYe Energy Storage Station
5 MWh
Project Capacity
COD：2022.08
DongGuan City, Guang Dong Province
eBlock 172
2.5 MW
用户侧
Application Type: C&I
Economic Model: Peak-Valley Arbitrage, New Energy Consumption, Axilliary Service
Environment Feature： High Ambient Temperature, High Ambient Humidity

## Slide 32
LingNan Energy Storage Station
4.12 MWh
Project Capacity
COD：2022.09
ZhuHai City, Guang Dong Province
eBlock 172
2.06 MW
用户侧
Application Type: C&I
Economic Model: Peak-Valley Arbitrage, New Energy Consumption, Axilliary Service
Environment Feature： High Ambient Temperature, High Ambient Humidity

## Slide 33
ZheJiang WenZhou Energy Storage Battery Station
2.06 MWh
Project Capacity
COD：2022.12
Wen Zhou City, ZheJiang Province
eBlock 172
1.03 MW
用户侧
Application Type: C&I
Economic Model: Peak-Valley Arbitrage, New Energy Consumption, Axilliary Service
Environment Feature： High Ambient Temperature, High Ambient Humidity

## Slide 34
YiWu WenYuan Energy Storage Station
Project capacity
COD：2022.05
YiWu Cicty, Zhe Jiang Province
eBlock 172
用户侧
688 kWh
344 kW
Application Type: C&I
Economic Model: Peak-Valley Arbitrage, New Energy Consumption, Axilliary Service
Environment Feature： High Ambient Temperature, High Ambient Humidity

## Slide 35
THANK YOU！
Reliable Clean Power for All